St. George’s Institute

Electronic Document Preparation and Management

EDPM Portfolio – Specification

Instructions:

- Prepare the following Specification, following all instructed guidelines

Schon Architects

Beautiful Concepts!

Architect’s Specifications

# General

  - Summary

Contractor shall furnish, install, and finish a vinyl wallcovering as specified in the contract documents.

  - Sample

Contractor shall submit for the architect’s approval a sample of each texture, type, or color to be installed

  - Compliance

Submit certification that the manufacturer’s wallcoverings meet the architect’s specification. Submit documentation that the manufacturer’s wallcovering meets the federal certifications for wallcovering products CCC-408 D and CFFA-W-101-D

  - Warranty

Contractor shall supply the manufacturer’s written warranty against defects in workmanship for 5 years from date of installation. Submit manufacturers written warranty.

  - Delivery, storage, and handling

All necessary materials for installations including wallcovering, primer and adhesives must be delivered to the job site undamaged. All containers are to be clearly marked with the manufacturer’s identification label.

Store vinyl wallcovering rolls and materials in a clean, dry area where temperature and humify remain constant and within the manufacturer’s specification

  - Project Conditions

Environmental conditions must remain constant and over 65 degrees Fahrenheit for at least four days and throughout the installation and 4-7 days thereafter. Walls shall be finished to the architect specification and be free of surface defects and dirt. The contractor for the installation process must provide sufficient lighting and access.

- Products

  - Vinyl Wallcoverings

All Vinyl wallcoverings specified and installed shall meet the latest federal specification CCC-W-408_D and CFFA-W-101-D. Standards for vinyl coated fabric wallcovering. All types 1and type 11 wallcoverings specified shall contain mold and mildew inhibitors and pass the ASTMG21 testing for mold and mildew resistance. The ASTM-E84 test must be passed with the wallcovering mounted to common gypsum wallboard.

  - Flame and Smoke Characteristics

The Manufacturer shall certify that the vinyl wallcovering supplied meets federally specified limits for flame, smoke development and flash over according to the required ASTM-E84 and NFPA286 tests.

- Execution

  - Inspection

The contractor shall provide a complete copy of MontiScape’s current hanging instructions to the installer pertaining to the installation of the wallcovering. All installation must conform to manufacturer’s current installation instructions and product technical information

All labels shall be checked for accuracy by the installer to insure that the shipment is received as ordered.

  - Clean up and completion

Upon completion of work, remove all surplus material and debris from the work site. All work sites must be clean and orderly upon installation crew departure.